| WEBRA MODELLMOTOREN GmbH & Co. KG A-2551 ENZESFELD, Eichengasse 9 / AUSTRIA PHONE: ++43 (0)2256-81122-0 begin_of_the_skype_highlighting (0)2256-81122-0 end_of_the_skype_highlighting FAX: ++43 (0)2256-82306 begin_of_the_skype_highlighting (0)2256-82306 end_of_the_skype_highlighting e-mail : webra@webra-austria.at |  |  |
| --- | --- | --- |

AERO HELI CARBURETTOR SILENCER ACCESSORIES SPAREPARTS TECHNICS DOWNLOAD HOME

| AERO SPEED 25 SPEED 32 SPEED 36 50-P5 GT 55-P5 GT SPEED 61F Racing 61F C SPEED 70 F RACING 80F 91-P5 91-P5i SPEED 120 SPEED 120 X SPEED 120 XP RACING 145 RACING 145 XP SPEED 150 SPEED 150i RACING 160 XP BOXER 30-2 FT-Glow |  | A = 41,00 mm B = 25,00 mm C = 96,00 mm D = 52,00 mm E = 103,00 mm engine Racing 61F C order no. 1030C volum ccm / cu in 9.95 / 0.61 power PS / KW 2.30 / 1.70 rpm 1/min 2500 - 18000 bore mm 24.00 stroke mm 22.00 weight g 445 system of control front intake porting Schnürle ballbearing 2 liner piston set ABC crankshaft M8 carburettor 1030/116 silencer tuned pipe 1100/230 accessories engine mount 3723 / 3730 glow plug 4303 airfilter 1100/92 spinner 1111/3 prop 11x6 / 12x8 |
| --- | --- | --- |